## Slide 1
Notes: <number>
Welcome to the next lesson in the game console class. In this lesson we will be studying computer architecture. I’m sure many of you are familiar with some common terms in the computer world such as CPUs, RAM, hard drives, etc. Although, this is all very good information to know, we will be studying a much lower level of computer architecture.
Concepts such as the differences between microprocessors and microcontrollers will be covered. Memory organizations such as Von Neumann vs. Harvard architecture will be detailed. We will talk about the internals of a microprocessor all the way down to the register transfer logic; that are essentially little micro programs that manage interactions.
By the end of the lesson and in the experiments we will begin working with SX-28 microcontroller. This is the heart of your game console. It will control everything including the video and sound operations. So we will start small and work with it in steps building upon knowledge from the past step. By the time the next lesson comes you will be prepared to understand how some example game console computer designs work. Let’s begin this lesson by first talking about microprocessors.

## Slide 2: Microprocessors
<number>
Lesson 5 - Computer Architecture
Control Unit
Arithmetic Logic Unit
Registers
Program Counter
Flags
ROM
RAM
I/O
Control Bus
Address Bus
Data Bus
A microprocessor is essentially a miniature computer that accepts instructions stored in memory and then executes them in sequential steps. It accesses external memory in the form of ROM and RAM. Input and Output devices may be connected to the microprocessor for controlling or reading values. A microprocessor also requires external power, reset circuitry, and usually an external clock.
Notes: <number>
A microprocessor is a miniature computer and if you have assembly programming knowledge then this is probably what you are most familiar with. Internally, a microprocessor is made up of different block devices. It will have a control unit that handles all the major operations and exchanges of data. The microprocessor will have some form of arithmetic logic unit, abbreviated ALU. The ALU will perform operations such as adding, subtracting, Boolean operations, and more. The ALU would be a very boring device if it didn’t have numbers to crunch on so we have registers that store the numbers to be operated on. You can write to and read from registers along with special registers that control functions of the microprocessor.
A microprocessor does not perform any functions with out a program so there is a program counter block that keeps a pointer to the current instruction being operated on. This program counter does not necessary have to count incrementally as we can use jump or branching instructions to change the flow of the program counter based on certain conditions. There are usually a number of flags that indicate the current state of a microprocessor. For example there is a flag that indicates when the addition of two binary numbers causes an overflow or carry of a number.
External to a microprocessor is required support hardware. For example we can connect a ROM memory storage device that will hold the program being run along with any saved data. In a Nintendo system the ROM memory would be a game cartridge that you plug into the NES to be run. Not only will it contain program code, but also art assets and maybe sounds to be played.
The number of registers a microprocessor has is usually pretty small; therefore, a larger ram bank is added to the microprocessor for storing state and game variables. Both of these devices are accessed through an address bus that indexes into the memory. A bus is just a term for a collection or grouping of wires. There is a data bus that is connected to the memory devices for retrieving and storing data. Normally, the address and data buses are shared between all memory devices and sometimes I/O devices. To handle the sharing of the bus lines a number of control wires are connected to enabled a single memory device at a time so there are no bus congestions.
Finally, a number of I/O devices can be connected to a microprocessor. In terms of a video game console these could be game controllers or the ever popular Dance Dance Revolution pads. A microprocessor is a synchronous digital electronic device so it requires a few extra connections such as external power, reset circuitry, and an external clock.

## Slide 3: Popular microprocessor
<number>
Lesson 5 - Computer Architecture
Intel 4004
The first processor released by Intel in 1970. 4-bit processor capable of running at 108KHz and has been deemed by some as the world’s first commercial microprocessor. Was originally created to be used in calculators but soon found favor in many applications.
Motorola 6800
Motorola’s first major attempt to get into the microprocessor market created in 1975. It is usually packaged as a 40 pin DIP. The 6800 was clocked up to 4 MHz and had two accumulators and may have been the first microprocessor to have an index register.
Motorola 6809
Developed in 1979 as a follow on processor to the 6800. It was used as the main CPU in systems such as the Tandy Color Computer as well as the Vectrex game console.
MOS 6502
8-bit processor created by MOS Technologies Inc. in 1975. At its time it was the least expensive processor on the market allowing it to be used in systems such as: Apple I, II computer, Atari 2600, 400, 800, Pet, Vic-20, Commodore 64, and of course the NES console system.
Zilog Z80
8-bit processor created by Zilog in 1976. Designed to run Intel 8080 code without modification so that it could swap out Intel easily. Some of the advantages included: single 5 volt power supply, easier clock generation circuitry, and of course cheaper. Used in systems such as: TRS80 Model I, II, III and the ever popular Game Boy and Game Boy color.
Notes: <number>
We are going to cover a number of popular microprocessors that helped define what it is. These early microprocessors have been used in everything from apple computers to the game boy hand held.
Motorola’s first attempt at a microcontroller was the Motorola 6800. This was released in 1975 and came packaged in a 40 pin DIP. The 6800 was capable of being clocked up to 4 MHz and had two accumulators. It is also speculated that this might have been the first microprocessor to have an index register for helping in operations that access memory. Motorola’s next attempt was developed in 1979 called the Motorola 6809. This was the main CPU used in systems like the Tandy color computer as well as the Vectrex gaming console developed by General Consumer Electric.
Intel released its first processor in 1970 called the Intel 4004. Many suggest that this is the very first microprocessor ever created. It is a 4-bit processor capable of running at 108 KHz. Designed originally for a customer of Intel to be used in a calculator, the processor showed so much promise that it replaced many different digital logic chips proving that a market for microprocessors existed.
The next processor we are going to talk about is without a doubt the most popular microprocessor in history. Created in 1975 by MOS Technologies the 6502 was an 8 bit processor. At the time it was the least expensive processor on the market which helped it get into systems like the Apple I, and II computer, the Atari 2600, 400, and 800. Also it made its way into the Pet, Vic-20, Commodore 64, and of course the beloved Nintendo Entertainment System.
The last microprocessor we will discus is the Zilog Z80. This is an 8-bit processor created by Zilog in 1976. The company was founded by designer Federico Faggin who helped design many of Intel’s microprocessors including the Intel 8080. The processor was designed so that it could swap out the Intel 8080 and be a cheaper alternative. Some advantages it had over other microprocessors at the time was its single 5 volt power supply and easier clock generation circuitry. One interesting history note is that the Z80 had a number of other assembly instructions discovered and used after it was produced for years. The reason why these instructions were not documented was because they were placed on the outer perimeter of the silicon chip. It turned out that a lot of these operations were damage so to increase chip yield in production houses they just did not document their functions. Later on as chip manufacturing abilities improved these operations were more reliable and you could write programs use the instructions. The Z80 was used in systems like the TRS80 Model I, II, and III. Also, it is the main CPU in the game boy and game boy color.

## Slide 4: Microcontrollers
<number>
Lesson 5 - Computer Architecture
Clock
Brownout
Detector
Microprocessor
Unit
RAM
Flash/ROM
Timers
UARTS
A/D
D/A
I/O Ports
Power
I/O Ports
Data and
Address Bus
(optional)
External
Interrupts
Serial I/O
Microcontrollers are simple because they typically have everything you need already built in – and more! They are usually made up of a microprocessor, RAM, Flash ROM, UART, A/D converter, PWM capture, and general purpose I/O pins. Thus, selecting a microcontroller is usually a simple matter of determining what peripheral devices and onboard flash/ram is needed, and then purchasing the chip.
Notes: <number>
A microcontroller can be thought of as a microprocessor with all the external support circuitry like RAM, ROM, and additional peripherals pulled inside the chip package. This makes for very tiny and simple embedded systems.
Added to the list of internal parts is usually a hardware UART that allows for serial communications between devices. Microcontrollers normally have an Analog to Digital sampling circuitry so that it can read in voltage values from external sensors. Timer circuitry is usually available since most microcontrollers are used in feedback control circuits. For example, you could use a microcontroller to control the temperature in your car. It would first sample a voltage value from a thermistor, or a thermal sensitive resistor. Then it will control the thermostat to either cool down the car or warm it up.
Because a microcontroller can do so many different things, the process of selecting one basically boils down to first determining what peripheral devices you want to connect to and what are your requirements for onboard RAM and ROM. We will be using a microcontroller for our game console because they are easy to get up and going but are still just as effective as a microprocessor.

## Slide 5: Popular microcontrollers
<number>
Lesson 5 - Computer Architecture
Microchip (PIC)
Simple 8-bit and up microcontrollers that are easy to use and have a large following. They are capable of large clock speeds some up to 40 MHz and more. Although, most instructions require 4 clock cycles for one operation so this effectively reduces the MIPs rating by ¼. Regardless, there are lots of tools and C compilers.
Ubicom/Parallax
Makers of the SX processors including the SX18, SX20, SX28, SX48, and SX52. With the SX52 being used in the XGS Micro Edition and the SX28 is the one we will use for our game console. Basically the next generation PIC processors where most instructions take a clock cycle or two.
Atmel
With products such as the AVR and ARM microcontrollers, Atmel has a strong following in developers and tool chains. Many microcontrollers are capable of running assembly code created by GNU C compiler tool chains. The ARM processor has been licensed out to many different companies so you may have seem ARM microcontrollers by other companies.
Motorola HC6805/11/12
Motorola has created a line of microcontrollers from 8-16 bit. These devices have interesting instruction sets but are overly complicated, especially for startup.
Notes: <number>
There are numerous microcontrollers out there. Almost everybody these days have their own microcontroller. Some of the more popular microcontrollers include Microchip’s line of PIC controllers. A PIC microcontroller is a simple 8-bit and up device that is extremely easy to use and has a large backing community. They are capable of running at high clock speeds with some running up to 40 MHz and more. The only thing that I believe is misleading is that a single instruction requires four clock cycles or more to operate. This effectively reduces the millions of instructions per seconds rating by ¼.
Next on the list is Ubicom and Parallax’s line of SX processors. This includes the SX18, 20, 28, 48 and the SX52. The SX52 is currently being used to power the XGameStations Micro Edition while the SX28 is the microcontroller we will be using in our game console. The difference between the two is simply decreased pin count, RAM, and ROM. The SX processors can be thought of as a competing PIC processor that can run up to 80 MHz or more an instead of 4 clocks per instruction they only require one clock for simple instructions.
Atmel has a line of microcontrollers named the AVR and ARM microcontrollers. They have a very strong following of open source programmers who have developed and use nice tools and free tool chains. Many of the microcontrollers are capable of running assembly code created by GNU C compilers and linkers. You may have seen the ARM processor but by a different company selling it. This is because the ARM architecture has been licensed out to many different companies but they still use the term ARM in the title of their products.
Last is Motorola’s line of microcontrollers with the HC6805 11 and 12. These range form 8 to 16 bit microcontrollers. The devices have a really interesting instruction set but they are overly complicated especially when writing startup sequences.

## Slide 6: Assembly Language – Machine Code
<number>
Lesson 5 - Computer Architecture
Assembly Language – is the lowest level of human readable notation for machine code. Almost all programmers working with microprocessors and microcontrollers have a working knowledge of assembly as each processor may contain different instructions.
Example:
MOV W, #FF ;loads hex 0xFF into W register
INC W ;increments W register
Machine Code – is a pattern of bits that encodes a machine operation understood natively by a microprocessor. Each assembly instruction is a mnemonic for a specific machine code value.
Example:
10110000 01100001
The above is an example of an X86 machine code instruction for the assembly viewed here:
MOV al, 061h
This moves a hexadecimal value 0x61 into the processor register named “al”.
CISC and RISC instruction sets:
-Emphasis on hardware vs. software
Complex instructions vs. reduced simple instructions only
Small code sizes vs. low cycles per second
Notes: <number>
Of course a microcontroller or microprocessor is nothing with out a procedural set of instructions called a program to run. Assembly language is the lowest level of human readable programming. The beauty of working with assembly code is that the instructions are tailored specifically for the processor you are working with. A lot of people will cringe when you start talking about programming in assembly code, but the truth is that assembly code is very simple. There is no mystery. Each instruction does exactly what it says and nothing more. Unlike C++ programming where you can override operators and make it so that a plus sign really acts like a minus sign.
When you are working with microprocessors and microcontrollers assembly programming is almost a must, so you will get plenty of opportunities for assembly programming in the next few lessons and experiments. An example of some assembly program is shown here. The first line of code reads as move to destination register W, the constant value #FF. This statement will load a hexadecimal value of 0xFF into the W register. The next instruction calls for the processor to increment the W register by one count.
When assembly code is ready to be loaded onto a processor it first needs to be assembled or translated into machine code. Machine code is a pattern of bits that encodes a machine operation understood natively by a microprocessor. Thus each assembly instruction is on a mnemonic for a specific machine code value. In the example at the bottom is a set of binary numbers that is a specific machine code for an X86 processor. A processor will read the first portion of bits and translate it in to a MOV instruction. The rest of the bits describe the register that is the destination address along with the constant value to be stored.
Now there are two ideas of thought when it comes to instruction sets for different processors. One thought is to create complex instructions that do many nifty things. This way a developer can call a single assembly instruction that will move lots of data around and perform a plethora of operations decreasing the overall code size. These instructions run on a computer classified as a Complex Instruction Set Computer or CISC. The nice advantage for this is that the processor can be optimized to perform these operations very fast. All Intel X86 computers run a CISC architecture.
The other way of thinking is to create a number of simple instructions that do very little. In this methodology the software is relied on heavily for optimizing. This idea came about when designers discovered that when programmers were writing code for CISC computers they would only use a fraction of the total instructions available, so they concluded that a reduced set of instructions may be more optimal. These instructions run on a Reduced Instruction Set Computer or RISC. Common processors that run this type of instruction set include the ARM, SPARC, and IBM’s power PC.

## Slide 7: Von Neumann vs. Harvard
<number>
Lesson 5 - Computer Architecture
Control
Unit
ALU
Registers
Single Unified
Memory
Data and Code
Input/Output
Processing Unit
Memory
I/O
Von Neumann
The Von Neumann architecture accesses memory that stores both the data and code in unified memory. Instructions are operated on sequentially.
-Allows for self modifying code
-Does NOT allow for simultaneous data and code access
Code Memory
Microprocessor
Input/Output
Harvard
The Harvard architecture splits the physical memory between data and code. This allows parallel accessing of data and code.
-No self modifying code
-Allows for simultaneous data and code access
Data Memory
Control
Unit
ALU
Notes: <number>
When it comes to memory organizations there are two popular methods. The first is the Von Neumann architecture named after Hungarian mathematician John Von Neumann. In this memory design model a single unified memory unit holds both code and data. To change the programs you would have to rewire or redesign the machine that is running. The term stored-program computer can be considered synonymous with this design. The Von Neumann memory design can still be found today in simple computing devices like a calculator.
Some early computers that ran the Von Neumann architecture include: IBM SSEC demonstrated in 1948, the ENIAC, and the Manchester SSEM. Since code and data are not separated this scheme does not support simultaneous access for both data and code. One thing it did allow for was self modifying code as this was important for changing code to change memory addressing locations. But the creation of index registers and indirect addressing made this feature obsolete.
The other memory architecture is called the Harvard architecture. In this design methodology data and code space is separated. The architecture was named the Harvard architecture because the first computer to use this approach was the Mark I relay-based computer that was first delivered to Harvard University for use. Some of the advantages are that you can access simultaneously data and code and also it is also easier to change programs without having to rework the system.
In modern computer design both approaches are used. Internal to the CPU uses a Harvard approach to access both code and data. Outside the CPU in ram and hard disk a Von Neumann approach is used to allow both data and code space to be saved together. Simple microcontrollers like the PIC, AVR, and the SX will use the Harvard architecture exclusively.

## Slide 8: Endianness
<number>
Lesson 5 - Computer Architecture
Endianness refers to the byte order of multi byte values and how they are stored in memory. To understand byte order you must first understand what the most significant byte (MSB) and least significant byte (LSB) mean.
The most significant byte represents the byte value that if changed will affect the multi byte value the most. Least significant byte on the other hand affects the multi byte value the least.
In a Big Endian memory addressing scheme the most significant byte of a two byte value is stored first. This is then followed by the least significant byte.
Little Endian on the other hand stores the least significant byte first followed by the most significant byte.
Notes: <number>
One thing we have to cover is stored memory Endianness. A lot of you may have heard the terms big endian and little endian but may not know exactly what it means. Endianness refers to the byte order of multi byte variables and how they are stored in memory. To understand byte order we must first define what it most significant byte (MSB) is and what least significant byte (LSB) means.
The most significant byte is the byte that if changed will impact the multi-byte number in the biggest way. When we write out binary numbers on paper in, for example, FE 71 the byte to the left FE is the most significant byte. The least significant byte is 71 and it is the value that if changed would have the smallest effect on the overall number.
Now Endianness comes in two forms: big endian and little endian. In big endian organization the most significant byte is placed first in memory and the least significant byte is placed last. One advantage for doing it this way is that it is easier for humans to read as the value is indexed through memory since we are used to seeing numbers read from left to right or most significant to least significant. Take a look at the image to the left. On the top is a value 0xFE71 stored in memory. To help show this two hexadecimal numbers are broken out individually into single bytes. At memory location 0x1000 we would first see 0xFE and one location further we would see the value 0x71.
Little endian stores the least significant byte first and the most significant byte last. So in the image we see that 0x71 is placed at memory location 0x1000 and hex value 0xFE is place at memory location 0x1001. To be honest there really is no advantage between one or the other when it comes down to performance. Little endian is used in all Intel X86 processors so you will see little endian machines being the dominant Endianness in desktop computers.
The choice of using little endian or big endian memory scheme when designing a processor is really quite arbitrary. The term Endianness itself was taken from Jonathan Swift’s novel “Gulliver’s Travels”. In the book Gulliver finds a nation with two factions arguing over which end of a boiled egg needs to be cracked open first. Of course this argument caused war.

## Slide 9: Register Transfer Logic
<number>
Lesson 5 - Computer Architecture
Register Transfer Logic is a pseudo language used by engineers to describe micro-operations performed by a processor. Engineers then transcribe RTL into hardware that creates the desired effect. A single assembly instruction may produce a number of RTL steps.
Register Transfer Logic Syntax
R1 <- R2
The above is a simple instruction that will cause the processor to copy the contents of register R2 to register R1.
LD: R1 <- R2
This RTL statement says that if there is a “load” command then copy the contents of register R2 to register R1. You can begin to see that by using RTL you can start to define and make your own processor, and detail out how assembly instructions and machine code will influence data registers. To show how you might do this look at the example operation below.
WEIRD: R1 <- R2 – 1, R2 <- R3 - 1
When the processor sees the machine code equivalent of the WEIRD assembly instruction it will first copy the contents of register R2 minus 1 to register R1. Then it will copy the contents of register R3 minus 1 to R2. This may seem like a really strange instruction, but if the processor that you are designing will require these operations often it might make sense to actually implement it.
Notes: <number>
We have talked about assembly language and how this is the lowest level programming language right above machine code. Well there is an even lower level descriptive language, almost like pseudo code that CPU developers use to describe the flow of data between registers in between clock cycles.
The RTL descriptive language is then translated to permanent hardware that creates the desired effect. Each RTL instruction can then be thought of as micro operations that describe how a processor works. A single assembly instruction may contain several RTL instructions.
Take a look at the first instruction: R1 left arrow R2. When this instruction, or the hardware that creates this instruction, is executed the contents of register R2 is copied into register R1.
The next example is LD: R1 left arrow R2. This RTL statement reads: “if the assembly command is a load command then copy the contents of register R2 into R1. There really are no set rules because you are designing a language that later on you will build through hardware. A few general guidelines have been created that allows other developers to more easily read your RTL language. For example the left arrow is a data copy instruction and we can also use commas to allow multiple instructions on one line like in the next example.
This example says “if the processor sees the equivalent machine code for the instruction called weird, the processor will copy the contents of register R2 minus 1 into the register R1. Also it will copy the contents of register R3 minus 1 into register R2.” This instruction may seem a little obtuse, but remember you are designing the processor and you are making all the rules. We won’t go into RTL language anymore than what was shown here but its important to know how CPU designers may work.

## Slide 10: External architecture
<number>
Lesson 5 - Computer Architecture
8/16/32
Data Bus
Address Bus
Control Bus
16
Memory
I/O
Clock
Interrupts
Microprocessor/
Microcontroller
Data Bus
The data bus is a collection of pins and wires that connect a data stream of information between the processor and the external system. A data bus is bi-directional and is usually 8, 16, or 32 bits wide. The most common use is to connect the data bus to memory. When the microprocessor is outputting data it is writing to memory, when it is inputting data it is reading from memory.
Address Bus
The address bus is another collection of lines that is used as an index into memory. The address bus is usually an output and each address location must index into a unique memory location. Therefore, a 16 bit wide address bus can index into 216 = 65,536 (64K) memory locations.
Control Bus
A control bus is a number of pins that control the external and internal system. The pins can be used for purposes such as: the input clock to the processor, interrupts, read and write control lines to memory banks, general purpose I/O control, bus control, power inputs, and more. A control bus is typically different for each processor.
Notes: <number>
The external architecture to a processor refers to the connections are created between processor, memory, I/O, clock inputs, and more. We have mentioned that a bus is nothing more than a collection of signal lines that perform the same general function. To interface with external components three buses are usually required including: Data, Address, and Control Bus.
The Data bus is a collection of wires that connect the data stream of information between the processor and external components. The data bus is a bi-directions bus that allows the processor to store or read values. If the data bus is connected to ram then the processor can send memory variables over the data bus to be stored temporarily in the ram. This bus is usually 8, 16, or 32 bits wide. When the microprocessor is outputting data is it said to be writing to memory, when it is inputting data is reading from memory.
The address bus is used for indexing into memory locations that can either reside in RAM or ROM. The address bus is used primarily for outputting and each address location must index into a unique memory location. So if a microprocessor has a total of 16 pins used for the address bus it can index into 2 raised to the 16 power that equals 65,536 memory locations.
The final bus used in the external architecture is the control bus. The control bus can have both inputting and outputting pins. It is typically used for selecting and enabling different memory banks and reading clock inputs for operating the processor. Other pins that are considered to be in the control bus include interrupts, power inputs, I/O control and more. A control bus can differ from processor to processor so you need to know what processor you are dealing with before knowing what the control bus looks like.

## Slide 11: Internal architecture
<number>
Lesson 5 - Computer Architecture
Key Terms
Data Width
Buses
ALU
Stack
Registers
Program Counter
Flags / Condition Code Register
Notes: <number>
The internal architecture for a processor will very more so than the external architecture between different processors. Although, processors will generally have the same key components. Take a look at the figure at the top of the slide.
In this figure we see that there is a single data bus that connects all the core components. This processor type would be called “a single bus architecture”. We see that this data bus ties together a program counter, stack pointer, a number of registers R0 through RN, and an arithmetic logic unit. When a program is executed the program counter will increment and the next assembly instruction will be operated on. If the assembly instruction is an addition operation between register R0 and the accumulator and the result is to be stored back into register R0 a number of operations will take place. First a control unit will transfer the contents of R0 into the right side of the ALU. A micro program sequencer will then instruct the ALU to add together the accumulator and the other value into it. When the addition has finished the ALU will update the status register so it can report certain status values like a carry for example. The results from the ALU addition will then travel down the single bus to be written back into register R0. You may see a disadvantage to the single bus architecture in that it can not read from registers at the same time it is writing to other registers. To overcome this problem designers have create multi bus architectures but we won’t cover this as it is discussed thoroughly in the book.
There are a couple of key terms that you should be familiar with. The first is the data width. The data width is a number that describes the internal width of all data related transactions. If for example the data width is 8 the register sizes will also be 8 bit wide and the ALU will be capable of operating on 8 bit values.
We have already spoken about buses, registers, and program counters so we won’t cover that again. The ALU is the arithmetic logic unit that is capable of performing operations like additions, subtractions, shift operations, and more. In most diagrams an ALU is represented by a V shape that indicates that two values are inputted and operations are preformed on and a single value is outputted at the bottom.
A stack is a space of memory where data and addresses are pushed and popped from. If you have done some assembly programming in the past you should be familiar with stacks. A simple example is when you make a function call in a program the return address is pushed on the stack. The function then operates and when it is finished the address on the stack is popped off and the program counter is set equal to the value. There are two different kinds of stacks: hardware and software. The hardware stack is created out of special registers that resides inside the CPU. Sizes for the hardware stack might include 4, 8, or 256. It is important to realize the size of the stack because this ultimately determines how many levels deep a function can recurse. A software stack is implemented in external system memory and in this case the CPU will have a stack pointer register.
The last thing to know about is that there exist flag or code condition registers. You can see one easily in the diagram called the status register that is tied to the ALU. Some other flag registers might include a register for controlling the Analog to Digital converter residing inside a microcontroller. Or maybe a register that determines how fast a timer counts for controlling I/O addons. In any case, knowing how a processor looks like on the inside will prepare you for working with low level languages like assembly code. When writing games for your game console you will need to have an understanding for most of these terms we have talked about.

## Slide 12: Pipelining
<number>
Lesson 5 - Computer Architecture
F D E W
F D E W
Fetch
Decode
Execute
Write
Typical Instruction Execution
F D E W
F D E W
F D E W
Instruction 1
Instruction 2
Instruction 3
Non-Pipeline Processor Sequence
F D E W
Instruction 1
Instruction 2
Instruction 3
Pipeline Processor Sequence
As shown above, pipelining a processor has huge speed improvements but there are a couple of potential problems. One problem arises when instruction 1 produces a result that instruction 2 requires. The output of instruction 1 won’t be ready until the write stage, but by the write stage instruction 2 is already executing from the old value. This can be solved by either rearranging instructions that do not depend on order or on each other (compilers can do this), or by placing NOP instructions until the write stage of instruction 1 is completed.
Notes: <number>
Instruction execution in classical processors typically contained four different stages. First there was a fetch stage that would go out and fetch the next instruction from memory. The next stage would look at the machine code of the instruction and decode it to determine what micro operations need to be performed and the required registers to operate on. In the execute phase the CPU performs the required operations like loading data from external memory or adding together two registers in the ALU. The final stage is the write back where the values produced in the ALU or data loaded from memory is written back into the appropriate registers.
Now if you were to execute an instruction one at a time the CPU has to wait until all the four execution steps are completed before continuing onto the next instruction. If each step required one clock cycle then it would take four clocks before you see the output of one instruction. Take a look at the top non-pipelined sequence to see this drawn out.
An optimization to the processor can be added called pipelining. When you pipeline a processor you construct the hardware in such a way that it will allows a second instruction to be started as soon as the first one enters the decode stage. After the second instruction enters the decode stage the third one begins the fetch. By the time the first instruction is in the write stage you could have 4 instructions in the pipeline. This is considered a 4 stage pipeline and it can significantly increase the throughput of the processor. Take a look at the Pipeline processor sequence in the center of the slide to view what this might look like.
Now there are huge improvements to be made by pipelining but there can also be potential problems. What if you had an instruction that adds two numbers together and saves the results into register 0 and the second instruction uses the result to perform some other operation. By the time the first instruction is has completed the write back stage the second instruction is already past the execution stage. There are a number of solutions to this problem. A compiler could place no operation instructions in between these types of instructions. A no operation instruction often shortened to NOP does exactly what its name says and performs no operation in the CPU. A better approach is for the compiler to rearrange instructions that do not require to be in order. Either way a pipeline processor still has a large speed up over a non pipelined processor.

## Slide 13: Caching
<number>
Lesson 5 - Computer Architecture
Microprocessor
External Cache
Main Memory
Very Fast
Fast
Slow
Microprocessor
Main Memory
External Cache Only
Internal Cache Only
L1 Cache
Microprocessor
Main Memory
Internal and External Cache
L1 Cache
External Cache
L2
Microprocessor
Main Memory
Internal L1 and L2 Cache
L1 Cache
Core
L2 Cache
Notes: <number>
Caching is a way to increase performance in a computer system. The idea of caching is very simple in fact almost common sense. A cache is a secondary memory storage that is placed between the microprocessor and external system memory. The thought is that accessing a small amount of cache is much faster than accessing the large system memory. There are a number of different caching schemes and we’ll go through some of them.
The first idea is to have the cache external to the microprocessor. This will sit between the microprocessor chip and the main memory. Remember that the cache is smaller than main memory so when the processor requests memory that is not currently in the cache it will require flushing of the cache and rewriting. Also when data is written to cache it will eventually need to be written out to main memory. These can become complicated tasks but they are not impossible.
Another idea is to place the cache so that it is internal to the microprocessor. The L1 in the figure stands for level 1 cache as you will find out soon that we can have different levels.
It used to be that caches were both external and internal in systems. So you might have an L1 internal cache of 16 K bytes that is extremely fast and then externally the L2 level two cache would be made of a larger 512K that is slightly slower. The level 2 cache always contain the original unmodified contents of the level 1 cache plus some extra memory that has either temporal or spatial locality. Temporal locality meaning that the code or data accessed at one time will probably be accessed again soon. Spatial locality means that data or code is more likely to be accessed if other code or data near it has just been accessed. On the outside of the level 2 cache is the main memory which can be something like a gig of ram for a desktop computer.
Another option for placing caches in a system is to place two levels of cache directly inside the processor. The idea is the same as having one internal and one external except now a processor has faster accessing times to the level 2 cache because it does not have some of the negative side effects of wire traces and board capacitances, etc. Remember the good old RC circuit? The processor we will be using for creating our game consoles does not have a caching structure to it but it is still good information to know for future projects.

## Slide 14: Addressing modes
<number>
Lesson 5 - Computer Architecture
Implied Addressing
In this addressing mode the operand implies the address.
Example: INC
Register Addressing
This mode uses the registers as the address.
Example: MOV R2, R1
Immediate Addressing
The operand for the instruction immediately follows the instruction.
Example: MOV R4, #$FE
Direct/Absolute Addressing
Instruction specifies the memory address as an absolute address.
Example: LDA $1000
Indexed Addressing
A base address is used as a starting point with an index added to it.
Example:
LDX #X_INDEX ;load the x index register
LDA player, x ;accumulator = player[x]
Relative Addressing
Relative addressing is usually used in branch and jump instructions where if a condition is meet the instruction pointer (IP) is incremented by a relative amount.
Notes: <number>
There are a few basic memory accessing modes that are prevalent in almost all microcontrollers or microprocessors. Some may have other strange schemes but they are based off the different addressing modes we will talk about now.
The first type of addressing is the implied addressing. Implied addressing, also known as inherent addressing, means that the operand or instruction already implies the address. An example is the increment instruction that increments the accumulator on a processor when no other operands are given. Thus, the instruction has an implied operand of the accumulator.
Register addressing means that the registers given in the instruction are the source and destination addresses. The example given moves one register to another register so the addressing mode is register addressing.
Immediate addressing places the operand for the instruction immediately following the instruction. For example the instruction MOV to register four the immediate hex value constant FE. Notice how the # sign prefixes the $ FE. The # sign is a directive to the assembler to signify immediate addressing and the $ sign says that the constant is a hexadecimal value.
Direct or absolute addressing means that you want to load or store the data with the given address in the instruction to the particular memory location. The example given is a load accumulator instruction that loads data from memory location hex 1000.
Indexed addressing is used when you want to have a base address and then index into that base address for accessing memory. This would be the standard approach for accessing an array of data like an array of memory that stores enemy health. You can then increment the index to cycle through all the different health values and find any values that are at zero. The example given in the slide first loads an x offset into the X index register. Then it loads the accumulator with the memory located at base address player plus x index register offset.
Relative addressing is usually used in branch and jump instructions where if a condition is met the instruction pointer or program counter is incremented by a relative amount. We will see some examples of relative addressing when we start to work with assembly code for the microcontroller in the experiments to come.

## Slide 15: Interrupts
<number>
Lesson 5 - Computer Architecture
Interrupts are an event that occurs that stops the normal flow of the program. There are two kinds of interrupts that we will consider: hardware and software.
Hardware Interrupts
Hardware interrupts are caused by external hardware that is attached to an external processor pin. When an interrupt occurs the current program counter address plus one is stored off for returning and the processor jumps to an Interrupt Service Routine (ISR). The ISR could contain complex or simple code; regardless when it is finished it will jump back to the stored program counter address.
Software Interrupts
Software interrupts function almost the same as a hardware interrupt but the difference lies in how the interrupt was triggered in the first place. Software interrupts are generated, as the name says, in software or by somebody’s program code. Some processors even have an assembly instruction name INT that takes as a parameter the interrupt type. An example of this is the DOS operating systems assembly command INT 10H that would set the video mode on the 80xxx86 processors.
A microcontroller will often use timers and pre-scalars to the timers to cause an interrupt. A prime example of this is a software pulse width modulated signal for controlling servos. The microcontroller can have its internal timers set to time the width of the pulse code. When the interrupt is flagged a digital I/O pin can be raised high or low to create the PWM signal.
Notes: <number>
Interrupts may be a new concept to you if you have never worked with assembly programming or embedded systems before. An interrupt is an event that occurs and then stops the normal flow of a program. There are two kinds of interrupts that we will talk about: hardware and software.
A hardware interrupt occurs when some external pin on the processor is triggered by separate hardware. When the interrupt occurs the execution jumps to an interrupt service routine abbreviated ISR where a special routine of code is run. When the ISR is finished the trigger state for the interrupt is usually reset and the processor returns back to its normal program. Another thing to think about is what happens to all of the normal program’s registers and saved values when the execution suddenly switches over to an interrupt. The answer is a context switch. In a context switch the values stored in registers are temporarily saved and then restored when the interrupt finishes. This can sometimes be a costly process.
Software interrupts operate the same way as hardware interrupts but the difference lies with how the interrupt was triggered in the first place. Software interrupts are generated by user code. Some processors even have assembly instructions name INT that has an operand that specifies the type of interrupt you want to trigger. For example, the DOS operating system had a software interrupt triggered by assembly command INT 10H. This would set the video mode on x86 processors.
A microcontroller can assign interrupts to timers so that when the timer wraps it causes an interrupt. In this sense we can adjust the timer and pre-scalar so that an interrupt happens when we want it to. For example we can control a servo position by sending a pulse width modulated digital signal. This is fancy talk for saying that the digital signal’s width can change to encode data. A servo measures how long a 60 Hz signal has been logic high and depending on the time it will reposition the servo arm. So we can calculate where we want to position the servo and then adjust the timers in the microcontroller so that when the interrupt occurs we toggle the pin and wire attached to the servo.